## Slide 1
Modeling, Analysis, and Control of Interdependent Networks
Jianan Zhang

## Slide 2: Outline
Introduction
Theory: modeling interdependent networks
  Random geometric graph
    Percolation analysis
    Random and geographical failures
  General layered graph
    Network connectivity under failures
    Robust routing under failures
Applications of interdependent networks
  Interdependent power grid and communication network
  Distributed computing networks
Future work

## Slide 3: Interdependent networks
Two Networks A & B are interdependent if the operation of Network A depends on operation of Network B and vice versa
Power Grid
Communication Network
Gas Network
Monitoring & Control of substations
Electricity for Routers
Electricity for Pumping Gas in Compressor Stations
Fuel for Gas Turbines
Transportation
Transporting Coal for Turbines using Railroads
Electricity for Railroads
Monitoring & Control of Pipelines
Monitoring & Control of Railroads
Electrical Vehicles
How to model interdependence and the impact of failures?

## Slide 4: Example of power and communication
Dependency in Italian power grid and communication networks
  Power grid: electricity for network routers
  Communication networks: control of power substations
A large cascading breakdown may occur from small node failures
  A country-wide blackout in Italy, 2003 [1]
[1] S. V. Buldyrev, et al., “Catastrophic cascade of failures in interdependent networks,” Nature 2010.
(Power grid)
(Communication networks)
Initial node failure
Cascading failure
Cascading failure

## Slide 5: Cascades cause large scale failures
2003 Northeast Blackout (Aug 14)
  Initial power failure at 1:31pm
  Cascading failure impacts entire Northeast America from 4:11pm and lasts 2 days (50M people affected)
  Impacts on interdependent systems: communication, water supply, transportation, …
[Source: http://www.robynboehler.com/Blackout-2003]

## Slide 6: Examples of interdependent networks failures

## Slide 7: Related work
Interdependent random graph models (node-to-node)
  Each network is modeled as a random graph [Buldyrev, et al. 2010]
  Every node in one graph is interdependent with a node in another graph
  Mutual giant component
  Cascading failures due to interdependence
  Extensions: lattice models [Bashan, et al. 2013]
From: Bashan, et al. 2013

## Slide 8: Outline
Introduction
Theory: modeling interdependent networks
  Random geometric graph
    Percolation analysis
    Random and geographical failures
  Arbitrary graph
    Network connectivity under failures
    Robust routing under failures
Applications of interdependent networks
  Interdependent power grid and communication network
  Distributed cloud network
Future work

## Slide 9: Properties of physical networks
Different network scales:
  Two networks may have different node densities and average link lengths.
Geographical locations and proximity:
  Connection: nodes within a smaller distance are more likely to be connected.
  Interdependence: nodes receive power or control from nearby nodes.
One-to-multiple interdependence:
  A node may be supported by multiple nodes (from the other network), with improved reliability.
power grid
communication network

## Slide 10: Model
Random geometric graph (RGG):
  Nodes are generated by a Poisson point process of density in a plane.
  Links exist between nodes within connection distance .
Interdependent RGGs:
interdependent distance
top view

## Slide 11: Percolation of RGG
Components grow larger as node density increases
Percolation: a positive fraction of nodes are in the largest component

## Slide 12: Percolation of interdependent RGGs
Percolation
  Giant component in each graph (a connected component consisting of a positive fraction of nodes)
  Each node in one giant component is interdependent with at least one node in the other giant component.
Phase transition
  Mutual component grows larger as new nodes are added.
  If a mutual giant component exists for , then a mutual giant component exists for and for .
Percolation threshold of interdependent RGGs
  A pair of node densities, curve

## Slide 13: Analytical bounds on percolation thresholds
Theorem 1:
If satisfies
then the interdependent RGGs percolate, where .
Theorem 2:
If satisfies
then the interdependent RGGs percolate, where .
Map to independent bond percolation on a square lattice

## Slide 14: 99% confidence intervals for percolation thresholds
Study the robustness under random node failures using the curve

## Slide 15: Robust under geographical attacks
If the node densities are above the upper bounds on the percolation threshold, then the interdependent RGGs still percolate after removing nodes in a geographical region.
  We derived upper bounds on the percolation thresholds of interdependent RGGs by mapping to a lattice
  Changing the bonds/sites from open to closed in a finite area does not affect its percolation [Bollobas & Riodan, 2006]

## Slide 16: More general supply-demand relationship
The methods can be extended to more general supply-demand relationship
  Each node in one graph requires a deterministic number () of interdependent nodes in the other graph.
  Each node in one graph requires a random number of interdependent nodes in the other graph.
Based on the same mapping, change conditions for a site/bond in the discrete model to be open
  E.g., a site is open if there are at least nodes in in the cell that contains the site.
Degree-dependent inhomogeneous failures

## Slide 17: Summary
Summary
  An interdependent random geometric graph model for interdependent networks
  Percolation thresholds curve
  Extensions to general supply-demand relationship
  Robust under geographical failures
  Degree-dependent inhomogenous failures

## Slide 18: Outline
Introduction
Theory: modeling interdependent networks
  Random geometric graph
    Percolation analysis
    Random and geographical failures
  Arbitrary graph
    Network connectivity under failures
    Robust routing under failures
Applications of interdependent networks
  Interdependent power grid and communication network
  Distributed cloud network
Future work

## Slide 19: Key challenges
1. Analysis: How many nodes need to be removed in one network to disconnect the other network?
2. Design: How to design the interdependence to maximize the number of node failures that a network can tolerate?
Focus: On arbitrary finite-size graphs
a
b
c
d
1
2
3
4
Removing supply nodes 1 and 2 leads to the failure of demand node b, and disconnects the graph G1.
To answer these questions, we study a model where nodes in a demand network (G1) depend on nodes in a supply network (G2).
G1
demand network
G2
supply network
Notes: Consider two interdependent networks, where nodes in one network provide supply to the other network. After removing nodes in one network, some nodes in the other network may lose its supply nodes and fail, and the other network may become disconnected.
To study the impact of node failures in one network on the other network, we focus on “network connectivity” as a metric for network functionality. Given two interdependent networks, we study the minimum number of node removals in one network to disconnect the other network.
Moreover, we study the network design problem to assign the interdependence between two networks, to maximize the number of node failures that both networks can resist.
To simplify the presentation, we consider a demand network and a supply network, and study the impact of node removals in the supply network on the demand network.

## Slide 20: Model for interdependent networks
A demand node has one or more supply nodes, and it fails if all of its supply nodes fail.
Supply node connectivity (of G1): the minimum number of node removals in G2 to disconnect G1.
G1
demand network
G2
supply network
a
b
c
d
1
2
3
4
Notes: A demand node fails if it loses all of its supply nodes. For example, in the figure, removing supply nodes 1 and 2 leads to the failure of demand node 3.
We define supply node connectivity as the minimum number of supply node removals that disconnect the demand network. This generalizes the concept of “node connectivity” of a single graph. Supply node connectivity indicates the resilience of a network to supply node failures. A robust demand network should have a large supply node connectivity.

## Slide 21: Computing the supply node connectivity
Transformation to a colored graph (right)
The supply node connectivity equals the minimum color node cut in the transformed graph
  A color node cut is a set of colors that disconnects the graph
Objective (Q1): Computing the supply node connectivity (NP-hard)
  Formulate a mixed integer linear program (exact solution)
  Developed a provable efficient polynomial time approximation algorithm
    Complexity: O(|V|2.5|E|)
    Approximation ratio: q (maximum number of components in an induced graph from a single color)
Notes: The demand network can be transformed to a colored graph, where a node has k copies if it has k supply nodes, and each copy has a color which corresponds to the supply node. The supply node connectivity equals the minimum color node cut in the transformed graph.
Given a colored graph G with colored nodes and regular edges, a color node cut is a set of colors Cc such that the nodes with colors in Cc are a superset of a node cut of G. A minimum color node cut of G is a color node cut Cc min that has the minimum number of colors. The number of colors in Cc min is the value of the minimum color node cut.
Computing the supply node connectivity of a network is NP-hard. The problem can be reduced from the vertex cover problem. Computing the supply node connectivity of a pre-specified pair of nodes (a source-destination pair) is also NP-hard, which can be reduced from the hitting set problem.
We developed a mixed integer linear program (MILP) to compute the supply node connectivity of a network. The MILP formulation relies on the node potentials. Each node has a potential. Connected nodes have the same potential. If nodes in the same graph have different potentials, then the graph is disconnected. These conditions can be formulated as integer constraints.
We also developed a polynomial time approximation algorithm to evaluate the supply node connectivity, by contracting the connected nodes that have the same supply node to a single component and evaluate the (standard) node connectivity in the contracted graph.

## Slide 22: Assignment to maximize supply node connectivity
Designing robust interdependent networks:
  Given a demand network and a supply network, assign a fixed number of supply nodes to each demand node, to maximize the supply node connectivity of the demand networks (or an SD pair)
Example:
  The supply node connectivity of the SD pair is 1 in the left figure
  The supply node connectivity of the SD pair is 2 in the right figure
Notes: We now consider the network design problem to assign the interdependence between two networks, to maximize the number of node failures that both networks can resist. The objective is to design robust interdependent networks that can resist a large number of supply node failures.

## Slide 23: Algorithms for Max. supply node connectivity
Maximizing the supply node connectivity of an SD pair
  Path-based interdependence assignment
    Node disjoint paths do not share supply nodes
    The assignment maximizes the supply node connectivity of a source-destination pair
Maximizing the supply node connectivity of a network
  CDS-based interdependence assignment
    A connected dominating set (CDS) supports network connectivity, in analogous to a path supporting SD connectivity. Disjoint CDS do not share supply nodes
    (k / log2 n) disjoint CDSs in an n-node k-connected graph [Censor-Hillel, et al. 2014]
    The assignment approximates the optimal global supply node connectivity to within factor O(log2 n)
  Random assignment
    Randomly assigning interdependence approximates the optimal global supply node connectivity to within a constant factor O(1) for most graphs
Notes: We develop interdependence assignment algorithms to maximize the supply node connectivity. All these algorithms run in polynomial time.
  To maximize the supply node connectivity of a source-destination pair, we develop a path-based interdependence assignment algorithm. Nodes in a path can have the same supply nodes, while node disjoint paths do not share any supply node. The assignment maximizes the supply node connectivity of a source-destination pair.
  To maximize the supply node connectivity of a network, we develop a CDS-based interdependence assignment algorithm and a random assignment algorithm. CDS (connected dominating set)-based algorithm approximates the optimal global supply node connectivity to within factor O(log2 n). Randomly assignment approximates the optimal global supply node connectivity to within a constant factor for most graphs.

## Slide 24: Maximizing the supply node connectivity
Numerical results in Erdos-Renyi graphs
The assignment algorithms achieve near-optimal supply node connectivity
The assignment algorithms run fast (in near-linear time)
  For CDS-based assignment: O(m × polylog(m)), where m is the # of edges
  For random assignment: O(n), where n is the # of nodes
Number of Nodes (¦V¦) | Average Degree (2¦E¦/¦V¦) | Number of supply nodes per demand node | Optimal supply node connectivity | Connectivity achieved by CDS-based assignment | Connectivity achieved by Random assignment
25 | 5 | 4 | 6.8 | 6.6 | 6.5
25 | 10 | 4 | 20 | 18.6 | 17.8
50 | 10 | 2 | 7 | 6.8 | 6.2
Notes: We provide numerical results of the interdependence assignment algorithms. We tested the algorithms in randomly generated Erdos Renyi graphs. For each row, the results are averaged over 10 realizations of random Erdos Renyi graphs with given number of nodes and average degree.
The assignment algorithms almost achieves the optimal supply node connectivity.
The CDS-based assignment algorithm has run time O(m polylog m), where m is the number of edges. The random assignment algorithm run in linear time.
Future plans:
Connectivity augmentation
  More supply nodes for critical demand nodes
  Improve network reliability with limited supply budget

## Slide 25: Robust routing in interdependent networks
1: Evaluate the path reliability in the demand network
2: Find the most reliable path between a pair of nodes
G1
G2
A
D
C
B
demand network
supply network
Notes: Consider two interdependent networks, where nodes in one network provide supply to the other network. After removing nodes in one network, some nodes in the other network may lose its supply nodes and fail, and the other network may become disconnected.
To study the impact of node failures in one network on the other network, we focus on “network connectivity” as a metric for network functionality. Given two interdependent networks, we study the minimum number of node removals in one network to disconnect the other network.
Moreover, we study the network design problem to assign the interdependence between two networks, to maximize the number of node failures that both networks can resist.
To simplify the presentation, we consider a demand network and a supply network, and study the impact of node removals in the supply network on the demand network.

## Slide 26: Evaluation of path failure probability
Computing the path failure probability is #P-hard.
  Reduction from DNF (Disjunctive Normal Form) counting
  Union of clauses; where each clause is an intersection of literals
    Clause : demand node in the path
    Literals in supply nodes for
Polynomial time randomized approximation scheme
  Estimate failure probability to within a factor with probability
  Time complexity:
  is the path length is the number of supply nodes per demand node
Failure event =

## Slide 27: Evaluation of path failure probability
Special case: identically small supply node failure probability
Reliability indicators:
  : minimum number of supply nodes for a node in the path
  : the number of combinations of supply node failures that disconnect the path
3

## Slide 28: Finding the most reliable path (Small failure Prob)
Objective: optimizing reliability indicators
  Observation: Optimizing is more important than optimizing
Algorithm to find the most reliable path
  Find paths that maximize : largest capacity path algorithm (linear time)
  If more than one path, find one with the minimum (NP-hard)
Each demand node depends on two nearest supply nodes;
PF = 7.9686 ×
supply node demand node

## Slide 29: Finding the most reliable path (general case)
Approximation algorithm to find the most reliable path
  Compute the most reliable path assuming that demand nodes fail independently. Shortest path algorithm, O(|E|+ |V| log|V|)
Performance of the algorithm
  Approximation ratio:
    The failure probability of the path is at most times the failure probability of the most reliable path
  is the number of demand nodes that a supply node supports
  is the number of supply nodes that a demand node depends on

## Slide 30: Diverse routing
Diverse routing improves reliability by using two or more paths
1: Evaluate the failure probability of two paths
2: Find the most reliable pair of paths between a pair of nodes
G1
G2
A
D
C
B
demand network
supply network
Notes: Consider two interdependent networks, where nodes in one network provide supply to the other network. After removing nodes in one network, some nodes in the other network may lose its supply nodes and fail, and the other network may become disconnected.
To study the impact of node failures in one network on the other network, we focus on “network connectivity” as a metric for network functionality. Given two interdependent networks, we study the minimum number of node removals in one network to disconnect the other network.
Moreover, we study the network design problem to assign the interdependence between two networks, to maximize the number of node failures that both networks can resist.
To simplify the presentation, we consider a demand network and a supply network, and study the impact of node removals in the supply network on the demand network.

## Slide 31: Computing the failure probability of two paths
Small failure probability
Reliability indicators:
  -failure resilient: at least one path survives after any supply node failures
  : the number of combinations of supply node failures that disconnect both paths

## Slide 32: Finding a pair of reliable paths (Small P case)
Objective: optimizing reliability indicators
  Observation: optimizing is more important than optimizing
Algorithm to compute a reliable pair of paths
  Integer program
  Smaller cuts have larger weights. Minimize the total weights of cuts.
Each demand node depends on two nearest supply nodes; .
Seattle-Miami:
Note that the most reliable path (previous example) is not in the pair
supply node demand node

## Slide 33: Finding a pair of reliable paths (general case)
A heuristic to compute a reliable pair of paths
  1. Assume independent demand node failures.
  2. Find one path with the minimum failure probability.
  3. Find one augmenting path with the minimum failure probability.
The most reliable pair of paths
A pair of paths computed by the heuristic
 | optimal | heuristic
0.01 | 1.0388 | 1.0773
 | optimal | heuristic
0.01 |  | 

## Slide 34: Summary
Layered graph model for interdependent networks (supply and demand networks)
  Captures many realistic scenarios: e.g., power-comms, etc.
Developed methods to evaluate reliability of network and paths
Developed methods to find the most reliable path, and pairs of paths
  Improve reliability through diverse routing

## Slide 35: Outline
Introduction
Theory: modeling interdependent networks
  Random geometric graph
    Percolation analysis
    Random and geographical failures
  Arbitrary graph
    Network connectivity under failures
    Robust routing under failures
Applications of interdependent networks
  Interdependent power grid and communication network
  Distributed cloud network
Future work

## Slide 36: Power grid frequency control
Classic:
  Frequency regulation (to recover nominal frequency) and economic dispatch both require communication
Recent advance:
  Distributed control (communication between neighbors)
  Frequency regulation by adjusting power generation using local frequency deviation (smaller frequency -> more generation)
  Economic dispatch using the common frequency deviation information
Our contribution:
  Achieving both frequency regulation and economic dispatch using no/limited communication
  Characterizing the importance of communication, dependent on power grid topology and physical properties
    Breaking the hierarchy: Distributed control & economic optimality in microgrids (Dörfler, Simpson-Porco, Bullo 2014)
    Optimal load-side control for frequency regulation in smart grids (Mallada, Zhao, Low 2014)

## Slide 37: Model
Economic dispatch & Frequency regulation
  Minimize cost of adjustable power
  Power balance
  Optimal solution (ignoring power line thermal limits and generation constraints)
Network dynamics
  Swing equation
  Power line
Control
  Control the adjustable power for economic dispatch and frequency recovery, using power grid measurement information and communication
supply = demand

## Slide 38: Integral control policy
Adjust the controllable power by local frequency measurement
Intuition:
  The phase angel difference before and after the disturbance provides reference to the adjustable power
Theorem:
  For , the cost under the integral control is at most more than the optimal cost, where is the power disturbance at a bus, is the number of nodes, is the algebraic connectivity of , , and is the minimum power line susceptance.
: Frequency deviation (from nominal frequency)

## Slide 39: Performance of the integral controller
The integral controller achieves near optimal economic dispatch, if either of the following holds
  Power line susceptance is large
  Controller gain is small
Example:
1
3
2
4
5
7
8
6
9
10
5 units demand increase

## Slide 40: Tradeoff: convergence time and cost
A small controller gain is needed to achieve near-optimal economic dispatch
The convergence time increases as the cost decreases
Example: optimal cost 23.27
convergence time (s) | 100 | 200 | 300 | 500 | 1000
cost | 39.11 | 31.81 | 28.89 | 26.30 | 24.41

## Slide 41: Delayed control
Adjust power generations after a timeout period
Intuition
  The frequencies at different generators are nearly synchronized under primary droop control, after a timeout period
  The common frequency deviation serve as a reference to adjust power generations
, for
, for

## Slide 42: Delayed control
Faster convergence compared with the original integral control
  Benefit: a larger controller gain to achieve the same cost
  Cost: no control over a timeout period
original integral control, cost = 39.11
delayed control, cost = 27.57 (T = 30s)
Over 30% cost reduction at the cost of 30s longer convergence time.
Compare: 350s convergence time for the original control to achieve the same cost.

## Slide 43: Arbitrary convex cost
Virtual price
Notations:
  Marginal cost at generator when the generation is :
  Inverse function computes the generation amount to have the marginal cost
Intuition:
  The virtual prices are almost identical at all generators
  The marginal costs are almost identical
,
.
cubic cost

## Slide 44: Generator capacity constraint
Power generation capacity constraints
Suppose the adjustable power generation should be within
The control is modified to
,
.

## Slide 45: Control policy using communication
Communication exchanges marginal costs
: boundary nodes in a component of communication network (e.g., )

## Slide 46: Role of communication
Exchange marginal cost information
Reduce convergence time by allowing larger controller gains
Example:
  Full communication: convergence time: 200s; cost: 23.27
  No communication: convergence time: 1500s; cost: 23.56
Full communication
No communication

## Slide 47: Importance of individual communication link
The failures of communication links have less severe impact if the corresponding power line has large susceptance
Cost: 26.17
Cost: 34.36

## Slide 48: Summary
A decentralized integral controller that achieves both frequency recovery and economic dispatch
  Near-optimal economic dispatch if the line susceptance are large or the controller gains are small
  General convex cost
  Generator capacity constraint
  Delayed control
Communication reduces the convergence time

## Slide 49: Outline
Introduction
Theory: modeling interdependent networks
  Random geometric graph
    Percolation analysis
    Random and geographical failures
  Arbitrary graph
    Network connectivity under failures
    Robust routing under failures
Applications of interdependent networks
  Interdependent power grid and communication network
  Distributed computing network
Future work

## Slide 50: Distributed computing networks
A network supporting both communication and computation
  Service function chaining
  Video streaming
  Cloud/fog computing
Choose a server to serve the content
Real time communication

## Slide 51: Model
Graph represents a computing network
  Flow is processed at computation nodes
  Computation constraints at nodes
  Communication constraints at links
Computation node
Communication links

## Slide 52: Network flow in computing networks
A network flow
  from source to destination
  needs to be processed at a computation node
Computing the maximum flow from source to destination
  Linear programming (polynomial time)

## Slide 53: Robustness metric – Cut
Communication cut
Computation cut
Joint communication and computation cut
10 1 10 1 10 cut = 10, flow = 2
1 10 1 10 1 cut = 20, flow = 1
5
1
1
1
5
5
5
5
1
1
cut = 1 + 1 + 1 = 3
flow = 1 + 2 = 3

## Slide 54: Max flow min cut
Min joint cut is at most twice the max flow
  Proof using layered graph
Example: Min cut can be twice as large as the max flow
2
2
2
2
2
2
2
Max flow = 1
Min cut = 2
Max flow = 1
Min cut = 2
Directed graph
Undirected graph
Max flow = min cut, for classical flow network [Ford & Fulkerson, 1956]

## Slide 55: Summary
Models for interdependent networks
  Interdependent RGGs
  Layered graph model
Analysis of interdependent networks robustness and cascading failures
  Increase the resilience to node failure
  Robust routing
Applications
  Power grid monitoring and control using communication
  Distributed computing network, data center networks

## Slide 56: Summary
Modeling
Control
Analysis
Power grid frequency control [5]
Percolation [1,2]
Connectivity [3]
Interdependent RGGs [1,2]
Traffic control in distributed computing networks [6]
Layered graph [3,4]
Routing [4]
[1] Robustness of interdependent random geometric networks, Allerton, TNSE.
[2] Robustness of interdependent random geometric networks under inhomogeneous failures, WiOpt.
[3] Connectivity in interdependent networks, TON.
[4] Robust routing in interdependent networks, INFOCOM.
[5] Joint frequency regulation and economic dispatch using limited communication.
[6] Optimal control of distributed computing networks with mixed-cast traffic flows, INFOCOM.
Notes: To facilitate this goal, this project has three inter-dependent thrusts, Modeling, analysis, and control…
Mathematical tools:
Modeling & Analysis -> Graph theory, Random graphs, Probability theory, Percolation theory, Markov model, …
Modeling & Control -> Control theory, Game theory, Network survivability, Distribution algorithms, Combinatorial optimization, …
How to defend against large scale (WMD) attacks on interdependent networks
Approach: Divide and conquer strategy…

## Slide 57: Future work
Design
Operation
& control
Reinforcement
Deployment
Understand the vulnerabilities of critical infrastructures and enhance their robustness
Improve the efficiency and performance of large-scale computing though tightly coupled compute, storage, and networks; power grid with renewable energies
Notes: Chen wenguang
Supercomputing
Wu JianPing
Cui yong
Li yong, 人流控制
Sigeminaxiang习总四个面向
Liu yunxin 张亚勤
Low carb
6G
Dianci kongjian yitihua. Tongxin sensor,
Lu mingquan, no GPS comm
Multi agent, tongxin dingwei daohang, daji
Medical engineering, care
Micro, wulidianzi. Optics
AI chip, optics computing
AD, DA, THz
Computing
0-》1
低碳，碳中和

## Slide 58: Backup slides

## Slide 59: Related work
Flow-based network models (network level interdependence)
  Power flow in power grids, failure dynamics [Parandehgheibi, et al., 2014, 2015]
  Communication failure in distributed control (economic dispatch in power grid) [Parandehgheibi, et al., 2016]
  Load re-distribution after failures, sandpile [Brummitt, et al., 2012; Yagan, et al., 2016]
Others (without network structures in the analysis)
  Empirical (history data after hurricanes)
  Agent based approach (assuming agent’s behaviors under various environment)
  System dynamics based approach (modeling system-level behavior by differential equations)
  Input-output model (economics, correlation matrix, linear relationship; can be generalized to non-linear relationship)

## Slide 60
Data-driven localization and estimation of disturbance in the interconnected power system

## Slide 61: Power line susceptance
Z=R+iX. Z: impedance. R: resistance. X: reactance
Y=G+iB. Y: admittance. G: conductance. B: susceptance
Y = 1/Z
Conductive line: R=0, G=0.
Resistive line: X=0, B=0.

## Slide 62: Power grid disturbance estimation
Disturbance: load increase
Frequency response after the disturbance
Observations:
  Frequency at generators (by PMUs)
Goals:
  Disturbance localization
  Disturbance magnitude estimation
load increase
frequency measurements

## Slide 63: Problem overview
Based on power grid transient state measurements (frequency deviations), estimate the disturbance location and magnitude
Impact: The estimation can be used for timely control (e.g., load shedding) to mitigate the disturbance or failure
Methodology: Model-free approach, machine learning
  Regression: linear regression for disturbance magnitude estimation
  Classification: logistic regression for disturbance localization

## Slide 64: Feature vector
Frequency deviations after the disturbance imply the disturbance magnitude
The frequency measurements are noisy (mHz)

## Slide 65: Conclusion
Estimate system disturbance/failure using transient state measurement
Machine-learning approach to estimate power grid disturbance location and magnitude
  Logistic regression for localization
  Linear regression for magnitude estimation
  Impacts of regularization, missing information (communication failure)
Impacts
  Much more accurate than equation-based approach
  Timely control to mitigate disturbance/failure

## Slide 66
Optimal control of distributed computing networks with mixed-cast traffic flows

## Slide 67: Background – service function chain
Service function chain
  Video streaming: firewall, transcoding, decoding
VF
VF
VF
VF
VF
VF
VF
1
2
3
4
source
firewall
encoding
transcoding
destination
decoding

## Slide 68: Model
Network model
  Computation/forwarding nodes (computation capacity )
  Communication links (transmission capacity )
A flow from to has to go through to be processed.

## Slide 69: Numerical result
Lower delay under UCNC, compared with backpressure algorithm
Commodity 1: 1 -> 11
Commodity 2: 4 -> 7
Computation nodes: 3, 8

## Slide 70: Numerical result
Mixed-cast simulation
  12 unicast and 6 multicast flows
  3 different service function chains
  Blue: treating a multicast flow as multiple unicast flows
  Red: mixed-cast flow under UCNC (throughput optimal)

## Slide 71: Conclusion
Universal Computing Network Control (UCNC)
  Jointly optimize packet routing and processing
First throughput-optimal algorithm for multicast service function chain traffic
Significantly lower delay compared with backpressure algorithm